Consolidation Potential for Small Water Systems — Differences Between

Urban and Rural Systems

Prepared By:  
Tom Ottem, Russell Jones, and Robert Raucher, PhD

Stratus Consulting Inc.

P.O. Box 4059

Boulder, CO 80306-4059

(303) 381-8000

tottem@stratusconsulting.com

May 15, 2003

National
   Rural Water 
   Association

# Executive Summary

Small drinking water systems often struggle to comply with new drinking water regulations because they lack the technical, financial, or management capabilities to significantly upgrade their water treatment processes. Consolidation (sometimes referred to as regionalization or cooperation) is advocated in some circles (including a recent National Drinking Water Advisory Council affordability panel) as a widely applicable solution to many of these small system problems.

While the concept has been widely advocated, there has been little empirical investigation on whether consolidation — either by physical interconnection or a shared management strategy — is an economically viable and feasible solution to the affordability issues faced by many small systems. A study for the Awwa Research Foundation (AwwaRF) in 1997 used geographic information systems (GIS) data from 17 states and found significant potential for small systems to share management and technical resources, but the cost to physically link systems would be prohibitive in almost all cases in most states. More recently, the U.S. Environmental Protection Agency in 2002 developed case studies of efforts to promote system consolidation in several states, listing several factors that improve the performance of state consolidation programs as well as barriers to system consolidation. Where possible, the costs and cost savings of consolidation projects were detailed; however, the available data did not allow for a rigorous cost-benefit analysis.

It is important to continue to empirically investigate the physical and economic dimensions of the issue to gain a better assessment of whether (and the extent to which) consolidation is or is not a viable approach to reducing small system costs. The research effort developed in this report takes advantage of advances in global positioning satellite (GPS) technology and GIS modeling since the time of the original AwwaRF study, and uses a much more complete dataset of system locations to reassess the economic feasibility of physically linking very small (25 to 500 served) and small systems (501 to 3,300 served) to larger systems. In addition, this effort investigates the physical proximity and socioeconomic differences between small water systems in rural and metropolitan areas.

The results of this study are summarized in Table S.1, and reveal the following:

- Over half of small systems (rural and urban combined) are located more than 7.5 miles from the nearest medium, large, or very large system (for very small systems, the median distance is approximately 6 miles). The data also show that small systems and very small systems are on average approximately 8.5 and 9 miles, respectively, from the nearest medium, large, or very large system.

| Table S.1. Summary of key statistics for small and very small water systems in rural and urban areasa |
| --- |
|  | Sample size | Distance (in miles) to nearest medium, large, or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
| System type |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 8,406 | 1.95 | 4.11 | 7.25 | 5.42 | 147 | 57 | 46,706 | 10.01% |
| Rural areas | 7,975 | 5.07 | 9.90 | 16.33 | 11.71 | 160 | 65 | 37,770 | 11.95% |
| All | 16,381 | 2.87 | 6.16 | 11.98 | 8.48 | 154 | 61 | 42,356 | 10.95% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 2,271 | 1.58 | 3.91 | 7.39 | 5.31 | 1,376 | 467 | 46,703 | 10.04% |
| Rural areas | 3,854 | 5.75 | 10.37 | 15.94 | 11.74 | 1,343 | 515 | 36,440 | 12.71% |
| All | 6,125 | 3.32 | 7.52 | 13.28 | 9.36 | 1,356 | 497 | 40,245 | 11.72% |
| a. Includes water systems in the following 34 states: AR, AZ, CA, CT, FL, GA, IA, ID, IL, IN, MA, MD, ME, MN, MO, MS, MT, NC, ND, NE, NH, NJ, NM, NY, OH, OR, PA, SD, UT, VA, VT, WA, WI, WV. Others excluded due to insufficient data. b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percentage of households in all census tracts within 10 miles of water system. |

- Significant differences exist between small water systems in rural areas and those in urban areas. For example, more than 50% of urban small systems are 5 miles or less from a larger system, but much fewer than 25% of rural systems are that close to a potential partner system. Since rural systems tend to be located much farther from a larger system than do small systems in urban areas, rural system costs for regional approaches probably will tend to be relatively high.

- Rural systems will most likely have a harder time paying for physical interconnections or other expenses. The household income of the populations served by rural small and very small community water systems is generally much lower (more than $8,000 per year less, for both size categories), and the poverty rate is higher (by 2 percentage points or more, for both size categories) than the urban populations served by small systems.

# 1.	Introduction

1.1	Background

Drinking water regulations often pose difficult problems for small water systems. On one hand, water providers want to meet their customers’ demands and provide the safest, highest quality water possible. On the other hand, water treatment often is expensive, especially on a per household basis in small systems (because of the economies of scale that exist for most water treatment technologies). When new drinking water regulations are enacted, providers often struggle to comply because they lack the technical expertise, training, or budget to install new treatment technologies or to otherwise upgrade their processes. This is especially true for small water systems, which have a relatively limited economic base (i.e., a small number of customers) from which to generate funds to pay for additional staff, training, equipment, or maintenance.

Since the Safe Drinking Water Act was first passed by Congress in 1974, a frequently suggested strategy for facilitating and reducing the costs of compliance for small systems has been to restructure them through regional consolidation or cooperation with other systems. Consolidation — whether by physical interconnection or a shared management strategy — would reduce unit costs by reducing duplication of effort and taking advantage of economies of scale. Regionalization has become widely advocated in some circles, including a recent National Drinking Water Advisory Council (NDWAC) panel assembled by the U.S. Environmental Protection Agency (EPA) to address small system affordability issues, as a highly valuable and widely applicable solution to many small system cost problems. However, there are limited data — and have been limited studies — on whether or not consolidation actually is as an economically viable and feasible solution to the affordability woes of many small systems.

## 1.2	Previous Studies

A study by the U.S. EPA (1993) of small water systems in three states (Alabama, South Dakota, and West Virginia) concluded that as many as 50% of small water systems could engage in some type of external restructuring to reduce the cost of meeting more stringent water quality requirements. The study also suggested that the most significant “barriers to consolidation and collaboration are emotional” and related to loss of autonomy. Other barriers noted in the study are misrepresentation and misunderstanding of costs and benefits and legal barriers. The study does not address barriers related to the costs of physically consolidating small systems (U.S. EPA, 1993).

Castillo et al. (1997) developed a study for the Awwa Research Foundation (AwwaRF) on the restructuring of small systems, using geographical location and other data available for water systems. These researchers found that physical interconnection between small and larger systems might be economically feasible for up to 35% of small systems in some states, but that in most states studied such consolidation would be economically viable for only 10% to 20% of small systems. This research also noted that because drive times between systems were often reasonable, larger systems probably could provide satellite (e.g., management) services and assistance to a high percentage (e.g., over 90% in many states) of neighboring smaller systems in an economically viable manner. Thus, this study generally found that there may be significant potential for small systems to share management and technical resources, but that the cost to physically link systems is prohibitive in almost all cases in most states. The study also found that the data available on the geographic location of facilities were poor, and as a result, included only 17 states in the analysis (Castillo et al., 1997).

More recently, in a report prepared for EPA, the Cadmus Group (2002) performed several case studies on efforts to promote system consolidation in several states. Where possible, the authors detail the costs and cost savings of consolidation projects. However, the data available did not allow for a rigorous cost-benefit analysis. From these case studies the authors compiled a list of several factors that improved the performance of state consolidation programs as well as a list of the barriers to system consolidation.

## 1.3	Overview of this Study

Other than as noted above, the issue of consolidation has not been widely or conclusively studied in an empirical manner. Nonetheless, consolidation remains an often advocated solution to small system problems. Therefore, it is important to continue to investigate the physical and economic dimensions of the issue so that we can gain a better assessment of whether (and the extent to which) consolidation is or is not a viable and promising approach to reducing small system costs and facilitating compliance.

The research effort developed in this report takes advantage of advances in GPS technology and GIS modeling since the time of the original Castillo et al. (1997) study and uses a more complete dataset of system locations to reassess the economic feasibility of physically linking small and very small systems to larger systems. In addition, the U.S. EPA (1993) and AwwaRF (Castillo et al., 1997) studies did not consider the potential differences in physical proximity, costs, and affordability that small water systems in rural areas may face as compared to small systems in more metropolitan areas. This study investigates the potential difference between rural and metropolitan areas by answering several questions for small water systems:

- What is the average physical distance from a small system to the nearest large system, in rural as opposed to in metropolitan areas?

- Are the number of persons and service connections served by small systems similar in rural and urban areas?

- Is there a significant difference in the incomes of customers of small rural water systems as compared to customers of small systems in more urban areas?

In this report, Section 2 describes the data used to analyze these questions and the methods used to assess data quality and to analyze the data. Section 3 presents the national level results, and state level results are included in Appendix B. Section 4 offers conclusions based on the results.

# 2.	Data and Methods

This section provides a brief overview of the data used and statistics calculated in this analysis. Further detail is provided in Appendix A.

## 2.1	Data

The water system and facility data used in this study were provided on special request from SDWIS/FED, EPA’s database of water systems (U.S. EPA, 2002a and 2002b). SDWIS/FED includes a variety of basic system data as well as data on specific facilities, including the latitude and longitude of each component of a water system.

Each system was categorized based on water system size. “Large” systems in this analysis are systems serving more than 3,300 persons, and “small” systems are those serving 3,300 or fewer persons. Only systems located in the continental United States were retained for analysis. A variety of tests were performed to ensure the accuracy of the latitude and longitude data.

Tables 1 and 2 present the number and percentage of systems by state that were included in the analysis. Table 1 contains data for small and very small systems. Table 2 contains data for medium, large, and very large systems. On the whole, reliable location data are available for roughly 85% of small and very small water systems. The percentage does vary by state, however. For example, location data are available for all small and very small systems in Connecticut, but are missing for approximately 90% of small and very small systems in Kansas. A similar result is found for medium, large, and very large systems — there are reliable location data for approximately 85% of systems in the United States, but data are missing for a large percentage of systems in certain states.

| Table 1. Number and percentage of very small and small systems without reliable location data — 2002a |
| --- |
| State | Number of systems | Number of systems with no match in location data | % of systems with no match in location data |
|  | Very small | Small | Very small | Small | Very small | Small | Total small, very small |
| AK | 347 | 62 | 8 | 0 | 2.3% | 0.0% | 2.0% |
| AL | 49 | 264 | 23 | 106 | 46.9% | 40.2% | 41.2% |
| AR | 217 | 371 | 73 | 108 | 33.6% | 29.1% | 30.8% |
| AZ | 504 | 191 | 23 | 8 | 4.6% | 4.2% | 4.5% |
| CA | 1,952 | 474 | 35 | 11 | 1.8% | 2.3% | 1.9% |
| CO | 581 | 204 | 139 | 19 | 23.9% | 9.3% | 20.1% |
| CT | 460 | 61 | 0 | 0 | 0.0% | 0.0% | 0.0% |
| DE | 171 | 51 | 85 | 26 | 49.7% | 51.0% | 50.0% |
| FL | 1,114 | 447 | 16 | 8 | 1.4% | 1.8% | 0.0% |
| GA | 1,153 | 302 | 194 | 24 | 16.8% | 7.9% | 15.0% |
| HI | 39 | 39 | 7 | 7 | 17.9% | 17.9% | 17.9% |
| IA | 633 | 393 | 124 | 69 | 19.6% | 17.6% | 18.8% |
| ID | 600 | 100 | 40 | 2 | 6.7% | 2.0% | 6.0% |
| IL | 692 | 683 | 1 | 2 | 0.1% | 0.3% | 0.2% |
| IN | 343 | 329 | 27 | 77 | 7.9% | 23.4% | 15.5% |
| KS | 493 | 344 | 434 | 316 | 88.0% | 91.9% | 89.6% |
| KY | 54 | 144 | 13 | 79 | 24.1% | 54.9% | 46.5% |
| LA | 522 | 416 | 99 | 58 | 19.0% | 13.9% | 16.7% |
| MA | 196 | 76 | 18 | 7 | 9.2% | 9.2% | 9.2% |
| MD | 330 | 109 | 9 | 10 | 2.7% | 9.2% | 4.3% |
| ME | 269 | 91 | 13 | 7 | 4.8% | 7.7% | 5.6% |
| MI | 779 | 411 | 300 | 148 | 38.5% | 36.0% | 37.6% |
| MN | 479 | 329 | 31 | 14 | 6.5% | 4.3% | 5.6% |
| MO | 842 | 429 | 127 | 82 | 15.1% | 19.1% | 16.4% |
| MS | 354 | 648 | 3 | 10 | 0.8% | 1.5% | 1.3% |
| MT | 530 | 100 | 35 | 4 | 6.6% | 4.0% | 6.2% |
| NC | 1,689 | 475 | 16 | 1 | 0.9% | 0.2% | 0.8% |
| ND | 188 | 109 | 53 | 21 | 28.2% | 19.3% | 24.9% |
| NE | 384 | 188 | 27 | 12 | 7.0% | 6.4% | 6.8% |
| NH | 556 | 94 | 17 | 9 | 3.1% | 9.6% | 4.0% |
| Table 1. Number and percentage of very small and small systems without reliable location data — 2002 (cont.)a |
| State | Number of systems | Number of systems with no match in location data | % of systems with no match in location data |
|  | Very small | Small | Very small | Small | Very small | Small | Total small, very small |
| NJ | 235 | 139 | 23 | 18 | 9.8% | 12.9% | 11.0% |
| NM | 434 | 122 | 175 | 36 | 40.3% | 29.5% | 37.9% |
| NV | 172 | 56 | 31 | 14 | 18.0% | 25.0% | 19.7% |
| NY | 1,917 | 617 | 495 | 167 | 25.8% | 27.1% | 26.1% |
| OH | 620 | 432 | 5 | 6 | 0.8% | 1.4% | 1.0% |
| OK | 621 | 412 | 317 | 145 | 51.0% | 35.2% | 44.7% |
| OR | 628 | 159 | 86 | 16 | 13.7% | 10.1% | 13.0% |
| PA | 1,344 | 502 | 10 | 4 | 0.7% | 0.8% | 0.8% |
| RI | 46 | 12 | 2 | 2 | 4.3% | 16.7% | 6.9% |
| SC | 369 | 155 | 25 | 39 | 6.8% | 25.2% | 12.2% |
| SD | 311 | 126 | 14 | 1 | 4.5% | 0.8% | 3.4% |
| TN | 151 | 265 | 70 | 121 | 46.4% | 45.7% | 45.9% |
| TX | 2,154 | 1,583 | 315 | 364 | 14.6% | 23.0% | 18.2% |
| UT | 243 | 116 | 23 | 8 | 9.5% | 6.9% | 8.6% |
| VA | 903 | 274 | 13 | 3 | 1.4% | 1.1% | 1.4% |
| VT | 323 | 89 | 32 | 2 | 9.9% | 2.2% | 8.3% |
| WA | 1,763 | 335 | 77 | 32 | 4.4% | 9.6% | 5.2% |
| WI | 634 | 313 | 24 | 13 | 3.8% | 4.2% | 3.9% |
| WV | 232 | 245 | 72 | 87 | 31.0% | 35.5% | 33.3% |
| WY | 203 | 47 | 34 | 5 | 16.7% | 10.6% | 15.6% |
| Total | 29,824 | 13,933 | 3,833 | 2,328 | 12.9% | 16.7% | 14.0% |
| a. Size category names follow those used by EPA in the SDWIS/FED database: very small systems are those serving 25-500 persons; and small systems serve 501-3,300. Sources: U.S. EPA, 2002a, 2002b. |

| Table 2. Number and percentage of medium, large, and very large systems without reliable location data — 2002a |
| --- |
| State | Number of systems | Number of systems with no match in location data | % of systems with no match in location data |
|  | Medium | Large | Very large | Medium | Large | Very large | Medium | Large | Very large | Total medium, large, very large |
| AL | 171 | 92 | 5 | 41 | 16 | 0 | 24.0% | 17.4% | 0.0% | 21.3% |
| AR | 96 | 43 | 1 | 20 | 6 | 0 | 20.8% | 14.0% | 0.0% | 18.6% |
| AZ | 52 | 41 | 8 | 1 | 3 | 0 | 1.9% | 7.3% | 0.0% | 4.0% |
| CA | 227 | 316 | 62 | 3 | 2 | 0 | 1.3% | 0.6% | 0.0% | 0.8% |
| CO | 60 | 54 | 8 | 17 | 16 | 1 | 28.3% | 29.6% | 12.5% | 27.9% |
| CT | 19 | 33 | 5 | 0 | 0 | 0 | 0.0% | 0.0% | 0.0% | 0.0% |
| DE | 15 | 7 | 2 | 8 | 3 | 0 | 53.3% | 42.9% | 0.0% | 45.8% |
| FL | 153 | 199 | 32 | 14 | 1 | 4 | 9.2% | 0.5% | 12.5% | 4.9% |
| GA | 112 | 85 | 12 | 11 | 9 | 2 | 9.8% | 10.6% | 16.7% | 10.5% |
| IA | 79 | 36 | 3 | 13 | 6 | 0 | 16.5% | 16.7% | 0.0% | 16.1% |
| ID | 28 | 13 | 1 | 0 | 0 | 0 | 0.0% | 0.0% | 0.0% | 0.0% |
| IL | 218 | 196 | 9 | 0 | 6 | 1 | 0.0% | 3.1% | 11.1% | 1.7% |
| IN | 120 | 68 | 5 | 25 | 9 | 0 | 20.8% | 13.2% | 0.0% | 17.6% |
| KS | 51 | 26 | 4 | 47 | 23 | 4 | 92.2% | 88.5% | 100.0% | 91.4% |
| KY | 141 | 97 | 3 | 68 | 32 | 0 | 48.2% | 33.0% | 0.0% | 41.5% |
| LA | 144 | 57 | 7 | 28 | 18 | 4 | 19.4% | 31.6% | 57.1% | 24.0% |
| MA | 87 | 152 | 8 | 4 | 29 | 0 | 4.6% | 19.1% | 0.0% | 13.4% |
| MD | 31 | 25 | 4 | 0 | 0 | 1 | 0.0% | 0.0% | 25.0% | 1.7% |
| ME | 19 | 12 | 1 | 1 | 1 | 0 | 5.3% | 8.3% | 0.0% | 6.3% |
| MI | 150 | 121 | 9 | 75 | 95 | 4 | 50.0% | 78.5% | 44.4% | 62.1% |
| MN | 70 | 77 | 2 | 2 | 5 | 0 | 2.9% | 6.5% | 0.0% | 4.7% |
| MO | 126 | 51 | 5 | 19 | 8 | 0 | 15.1% | 15.7% | 0.0% | 14.8% |
| MS | 137 | 47 | 1 | 2 | 0 | 0 | 1.5% | 0.0% | 0.0% | 1.1% |
| MT | 26 | 7 | 0 | 1 | 0 | 0 | 3.8% | 0.0% | na | 3.0% |
| NC | 131 | 98 | 8 | 3 | 0 | 0 | 2.3% | 0.0% | 0.0% | 1.3% |
| ND | 12 | 9 | 0 | 3 | 1 | 0 | 25.0% | 11.1% | na | 19.0% |
| NE | 28 | 12 | 2 | 1 | 1 | 0 | 3.6% | 8.3% | 0.0% | 4.8% |
| NH | 16 | 17 | 1 | 1 | 1 | 0 | 6.3% | 5.9% | 0.0% | 5.9% |
| NJ | 91 | 126 | 12 | 13 | 20 | 1 | 14.3% | 15.9% | 8.3% | 14.8% |
| NM | 32 | 26 | 1 | 5 | 3 | 0 | 15.6% | 11.5% | 0.0% | 13.6% |
| Table 2. Number and percentage of medium, large, and very large systems without reliable location data — 2002 (cont.)a |
| State | Number of systems | Number of systems with no match in location data | % of systems with no match in location data |
|  | Medium | Large | Very large | Medium | Large | Very large | Medium | Large | Very large | Total medium, large, very large |
| NV | 19 | 7 | 4 | 1 | 3 | 3 | 5.3% | 42.9% | 75.0% | 23.3% |
| NY | 177 | 128 | 20 | 37 | 19 | 3 | 20.9% | 14.8% | 15.0% | 18.2% |
| OH | 148 | 144 | 10 | 2 | 5 | 2 | 1.4% | 3.5% | 20.0% | 3.0% |
| OK | 80 | 42 | 4 | 15 | 2 | 0 | 18.8% | 4.8% | 0.0% | 13.5% |
| OR | 47 | 51 | 4 | 7 | 11 | 1 | 14.9% | 21.6% | 25.0% | 18.6% |
| PA | 180 | 128 | 15 | 1 | 0 | 1 | 0.6% | 0.0% | 6.7% | 0.6% |
| RI | 11 | 13 | 2 | 8 | 3 | 0 | 72.7% | 23.1% | 0.0% | 42.3% |
| SC | 83 | 61 | 4 | 26 | 15 | 1 | 31.3% | 24.6% | 25.0% | 28.4% |
| SD | 21 | 10 | 1 | 1 | 0 | 0 | 4.8% | 0.0% | 0.0% | 3.1% |
| TN | 147 | 100 | 5 | 39 | 16 | 0 | 26.5% | 16.0% | 0.0% | 21.8% |
| TX | 518 | 232 | 26 | 126 | 51 | 4 | 24.3% | 22.0% | 15.4% | 23.3% |
| UT | 48 | 41 | 7 | 3 | 3 | 1 | 6.3% | 7.3% | 14.3% | 7.3% |
| VA | 71 | 57 | 15 | 3 | 3 | 0 | 4.2% | 5.3% | 0.0% | 4.2% |
| VT | 23 | 7 | 0 | 0 | 0 | 0 | 0.0% | 0.0% | na | 0.0% |
| WA | 91 | 85 | 7 | 9 | 21 | 2 | 9.9% | 24.7% | 28.6% | 17.5% |
| WI | 95 | 64 | 4 | 5 | 15 | 2 | 5.3% | 23.4% | 50.0% | 13.5% |
| WV | 58 | 20 | 1 | 11 | 0 | 0 | 19.0% | 0.0% | 0.0% | 13.9% |
| WY | 13 | 9 | 0 | 4 | 3 | 0 | 30.8% | 33.3% | na | 31.8% |
| Total | 4,472 | 3,342 | 350 | 724 | 484 | 42 | 16.2% | 14.5% | 12.0% | 15.3% |
| a. Size category names follow those used by EPA in the SDWIS/FED database: medium systems serve 3,301-10,000; large systems serve 10,001-100,000; and very large systems serve over 100,000. Sources: U.S. EPA, 2002a, 2002b. |

## 2.2	Methods

To test the feasibility of physically consolidating small systems with nearby larger systems, we calculated the distance from each small system to the nearest facility in a large system. Distance was calculated to a central facility within the nearest system. Since there is no pre-defined central point, we prioritized the types of facilities in large systems and calculated distance by priority. We first checked for the presence of a nearby medium, large, or very large treatment plant (category 1). If multiple treatment plants were present within 25 miles, the distance was set equal to the minimum distance within the category. If no treatment plants were present within 25 miles, then we checked for facilities in category 2, and so on. The categories were prioritized as follows:

- nearest treatment plant within 25 miles

- nearest reservoir within 25 miles

- nearest storage facility within 25 miles

- nearest intake within 25 miles

- nearest well within 25 miles

- nearest pump facility within 25 miles

- nearest treatment plant, reservoir, storage facility, intake, well, or pump facility between 25 to 50 miles.

In cases where no facility in a medium, large, or very large system was found within 50 miles of a small system, that small system was eliminated from the analysis. This was done to avoid assigning large distances where such estimates might be an artifact of dataset limitations and omissions. This is a conservative approach in that it may understate distances because for some communities the nearest neighboring larger entity may indeed be more than 50 miles away.

In addition to the distance between systems, we used SDWIS/FED data (U.S. EPA, 2002a, 2002b), to compare the average population served and number of service connections. We also used data from the 2000 Census (U.S. Census Bureau, 2003), to classify systems as rural or metropolitan and to compare average income levels and poverty rates in the area in a 10-mile radius surrounding systems.

# 3.	Results

The primary goal of this analysis was to take advantage of advances in GPS technology and GIS modeling and improved location data to investigate the potential differences in physical proximity, costs, and affordability that small water systems in rural areas may face as compared to small systems in more metropolitan areas. We analyzed the location and system data to answer the following questions for small water systems:

- What is the average physical distance from a small system to the nearest large system, in rural as opposed to in metropolitan areas?

- Are the number of persons and service connections served by small systems similar in rural and urban areas?

- Is there a significant difference in the incomes of customers of small rural water systems as compared to customers of small systems in more urban areas?

Table 3 presents the summary results from this effort for the national level (state-level results are provided in Appendix B). In Table 3, results for several statistics are reported by size category (very small and small) for both urban and rural water systems throughout the United States. Because of physical distance, small and very small community water systems are likely to face relatively high costs to connect to larger systems. Over half of small systems, are located more than 7.5 miles from the nearest medium, large, or very large system. For very small systems, the median distance over 6 miles. For both size categories, however, a large number of systems are much farther from larger systems. Small systems and very small systems are on average located approximately 8.5 miles or more from the nearest medium, large, or very large system. More than 25% of systems in both size categories would have to connect to a larger system that is 12 or more miles away.

In addition, the results indicate that there are, in fact, some very noticeable differences between small water systems in rural and urban areas. Since rural systems tend to be located much farther from a larger system than are small systems in urban areas, their costs for any regional approaches will tend to be much higher. The difference in average and median distance for both the small and very small categories is striking. Approximately half of the very small systems in urban areas are less than 4.5 miles from a larger system. In rural areas, less than 25% of the systems are within 5 miles. For small systems a similar pattern is evident — more than 50% of urban systems are 3.9 miles or less from a larger system, but fewer than 25% of rural systems are within 5.8 miles of a potential partner system.

At the same time, rural systems will most likely have a harder time paying for potential physical interconnections. The household income of the population served by rural small and very small community water systems is generally much lower (more than $8,900 per year less, for both size categories), and the poverty rate is higher (by 2 percentage points or more, for both size categories) than in the population served by small and very small urban systems. These demographic results are quite similar to those reported by Rubin (2001), who prepared a similar, but more detailed, analysis of income and poverty using 1990 Census data.

State level results are presented in Appendix B.

# 4.	Conclusions

Because of physical distance, small community water systems are likely to face relatively high costs to connect to larger systems. These costs may pose a more significant barrier to consolidation than suggested by previous research efforts. Since rural systems tend to be located farther from a larger system than are small systems in urban areas, their costs will be even higher. At the same time, rural systems are likely to have a harder time paying for these types of connections because the income of the population served by rural small community water systems is generally not as high as it is for urban systems.

| Table 3. Summary of key statistics for small and very small water systems in rural and urban areasa |
| --- |
|  | Sample size | Distance (in miles) to nearest medium, large, or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
| System type |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 8,406 | 1.95 | 4.11 | 7.25 | 5.42 | 147 | 57 | 46,706 | 10.01% |
| Rural areas | 7,975 | 5.07 | 9.90 | 16.33 | 11.71 | 160 | 65 | 37,770 | 11.95% |
| All | 16,381 | 2.87 | 6.16 | 11.98 | 8.48 | 154 | 61 | 42,356 | 10.95% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 2,271 | 1.58 | 3.91 | 7.39 | 5.31 | 1,376 | 467 | 46,703 | 10.04% |
| Rural areas | 3,854 | 5.75 | 10.37 | 15.94 | 11.74 | 1,343 | 515 | 36,440 | 12.71% |
| All | 6,125 | 3.32 | 7.52 | 13.28 | 9.36 | 1,356 | 497 | 40,245 | 11.72% |
| a. Analysis includes water systems in the following states: AR, AZ, CA, CT, FL, GA, IA, ID, IL, IN, MA, MD, ME, MN, MO, MS, MT, NC, ND, NE, NH, NJ, NM, NY, OH, OR, PA, SD, UT, VA, VT, WA, WI, WV. Others excluded due to insufficient data. b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percentage of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

# References

Cadmus Group. 2002. Small Drinking Water Consolidation: Selected State Program and Consolidation Case Studies. Prepared for U.S. Environmental Protection Agency by the Cadmus Group, Inc., Boston, MA.

Castillo, E., S.K. Keefe, R.S. Raucher, and S.J. Rubin. 1997. Feasibility of Small System Restructuring to Facilitate SDWA Compliance. Project #185. Prepared for American Water Works Association Research Foundation, Denver, CO.

Rubin, S.J. 2001. Criteria to Assess the Affordability of Water Service. White paper for National Rural Water Association.

U.S. Census Bureau. 2003. United States Census 2000. U.S. Department of Commerce Economics and Statistics Administration. ftp://ftp2.census.gov/census_2000/datasets/Summary_File_3/ Accessed February 10, 2003.

U.S. EPA. 1993. Technical and Economic Capacity of States and Public Water Systems to Implement Drinking Water Regulations. Office of Water. EPA-810-R-93-001. Report to Congress.

U.S. EPA. 2002a. FY2002 Public Water System Inventory data. Data from SDWIS/FED downloaded from http://www.epa.gov/safewater/data/detaileddetails. Accessed March 3, 2003.

U.S. EPA. 2002b. Safe Drinking Water Information System (SDWIS/FED). Data provided via special request, December 2002.

# Appendix A. Data and Methods

This appendix provides more detailed information on the data and methods used in this analysis.

#### A.1	Location Data

The locational data used in this study come from data provided on special request from SDWIS/FED, EPA’s database of water systems. SDWIS/FED includes fields for the latitude and longitude of each component of a water system (U.S. EPA, 2002b).

The dataset includes the following information for each water system at the facility level:

- water system number (PWSID)

- water system type

- water system name

- region

- state

- geography type

- groundwater/surface water designation

- primary source

- size category

- owner type

- population served

- number of service connections

- administrator contact info

- facility name

- facility type

- latitude position of facility

- longitude position of facility.

EPA provided data only for facilities for which latitude and longitude are available in SDWIS/FED.

#### A.2	System Data

We obtained more detailed data at the water system level from the SDWIS/FED data publicly available via EPA’s website. The website provides access to publicly available information. The most recent system data, from 2002, were downloaded (U.S. EPA, 2002a). The dataset includes the following information for each community water system:

- water system number (PWSID)

- water system type

- water system name

- region

- state

- primary county served

- primary city served

- primary source of water

- size category

- owner type

- population served

- number of service connections.

A.3	Quality Assurance Methods

We linked the location and system databases via the water system number (PWSID) field to facilitate calculating descriptive statistics. Before merging, the two databases were divided into “large” and “small” facilities based on the system size attribute. Large facilities are those serving more than 3,300 persons, and small facilities are those serving 3,300 or fewer persons. Only facilities located in the continental United States were retained for analysis.

After the two databases were created, we merged the corresponding tables using the PWSID attribute as a key field. GIS point layers were created from the resulting databases using the latitude and longitude attributes within the tables.

Two tests were performed on the accuracy of the latitude and longitude data. First, the resulting GIS data was overlaid with a GIS coverage of counties to examine the correspondence between the primary county served identified in the system data and the county where the latitude/longitude point is actually located. Since each water system (as determined by unique PWSID) might contain multiple facilities (wells, pump facility, treatment plant, etc.), all facilities in a water system were retained if any individual facility had a match between the county name in the database and either the same or adjacent county within the corresponding GIS dataset. Others were omitted. Second, in a similar manner, the latitude and longitude data for each facility was tested to ensure that the facility latitude/longitude data did not fall within a water body. All facilities with a latitude/longitude position falling more than one-half mile from the coastline into an ocean or one of the Great Lakes were eliminated from the database before the analysis.

The result of this screening process is two databases, one for small systems and one for large systems, that contain the latitude/longitude positions of facilities deemed to have data of sufficient quality to include in the analysis. Tables A.1 and A.2 present the number and percentage of systems by state that were included in the small and large system databases. On the whole, reliable location data are available for roughly 85% of small and very small water systems. The percentage does vary by state, however. For example, location data are available for all small and very small systems in Connecticut, but are missing for approximately 90% of small and very small systems in Kansas. A similar result is found for medium, large, and very large systems — there are reliable location data for approximately 85% of systems in the United States, but data are missing for a large percentage of systems in certain states.

| Table A.1. Number and percentage of very small and small systems without reliable location data — 2002a |
| --- |
| State | Number of systems | Number of systems with no match in location data | % of systems with no match in location data |
|  | Very small | Small | Very small | Small | Very small | Small | Total small, very small |
| AK | 347 | 62 | 8 | 0 | 2.3% | 0.0% | 2.0% |
| AL | 49 | 264 | 23 | 106 | 46.9% | 40.2% | 41.2% |
| AR | 217 | 371 | 73 | 108 | 33.6% | 29.1% | 30.8% |
| AZ | 504 | 191 | 23 | 8 | 4.6% | 4.2% | 4.5% |
| CA | 1,952 | 474 | 35 | 11 | 1.8% | 2.3% | 1.9% |
| CO | 581 | 204 | 139 | 19 | 23.9% | 9.3% | 20.1% |
| CT | 460 | 61 | 0 | 0 | 0.0% | 0.0% | 0.0% |
| DE | 171 | 51 | 85 | 26 | 49.7% | 51.0% | 50.0% |
| FL | 1,114 | 447 | 16 | 8 | 1.4% | 1.8% | 0.0% |
| GA | 1,153 | 302 | 194 | 24 | 16.8% | 7.9% | 15.0% |
| HI | 39 | 39 | 7 | 7 | 17.9% | 17.9% | 17.9% |
| IA | 633 | 393 | 124 | 69 | 19.6% | 17.6% | 18.8% |
| ID | 600 | 100 | 40 | 2 | 6.7% | 2.0% | 6.0% |
| IL | 692 | 683 | 1 | 2 | 0.1% | 0.3% | 0.2% |
| IN | 343 | 329 | 27 | 77 | 7.9% | 23.4% | 15.5% |
| KS | 493 | 344 | 434 | 316 | 88.0% | 91.9% | 89.6% |
| KY | 54 | 144 | 13 | 79 | 24.1% | 54.9% | 46.5% |
| LA | 522 | 416 | 99 | 58 | 19.0% | 13.9% | 16.7% |
| MA | 196 | 76 | 18 | 7 | 9.2% | 9.2% | 9.2% |
| MD | 330 | 109 | 9 | 10 | 2.7% | 9.2% | 4.3% |
| ME | 269 | 91 | 13 | 7 | 4.8% | 7.7% | 5.6% |
| MI | 779 | 411 | 300 | 148 | 38.5% | 36.0% | 37.6% |
| MN | 479 | 329 | 31 | 14 | 6.5% | 4.3% | 5.6% |
| MO | 842 | 429 | 127 | 82 | 15.1% | 19.1% | 16.4% |
| MS | 354 | 648 | 3 | 10 | 0.8% | 1.5% | 1.3% |
| MT | 530 | 100 | 35 | 4 | 6.6% | 4.0% | 6.2% |
| NC | 1,689 | 475 | 16 | 1 | 0.9% | 0.2% | 0.8% |
| ND | 188 | 109 | 53 | 21 | 28.2% | 19.3% | 24.9% |
| Table A.1. Number and percentage of very small and small systems without reliable location data — 2002 (cont.)a |
| State | Number of systems | Number of systems with no match in location data | % of systems with no match in location data |
|  | Very small | Small | Very small | Small | Very small | Small | Total small, very small |
| NE | 384 | 188 | 27 | 12 | 7.0% | 6.4% | 6.8% |
| NH | 556 | 94 | 17 | 9 | 3.1% | 9.6% | 4.0% |
| NJ | 235 | 139 | 23 | 18 | 9.8% | 12.9% | 11.0% |
| NM | 434 | 122 | 175 | 36 | 40.3% | 29.5% | 37.9% |
| NV | 172 | 56 | 31 | 14 | 18.0% | 25.0% | 19.7% |
| NY | 1,917 | 617 | 495 | 167 | 25.8% | 27.1% | 26.1% |
| OH | 620 | 432 | 5 | 6 | 0.8% | 1.4% | 1.0% |
| OK | 621 | 412 | 317 | 145 | 51.0% | 35.2% | 44.7% |
| OR | 628 | 159 | 86 | 16 | 13.7% | 10.1% | 13.0% |
| PA | 1,344 | 502 | 10 | 4 | 0.7% | 0.8% | 0.8% |
| RI | 46 | 12 | 2 | 2 | 4.3% | 16.7% | 6.9% |
| SC | 369 | 155 | 25 | 39 | 6.8% | 25.2% | 12.2% |
| SD | 311 | 126 | 14 | 1 | 4.5% | 0.8% | 3.4% |
| TN | 151 | 265 | 70 | 121 | 46.4% | 45.7% | 45.9% |
| TX | 2,154 | 1,583 | 315 | 364 | 14.6% | 23.0% | 18.2% |
| UT | 243 | 116 | 23 | 8 | 9.5% | 6.9% | 8.6% |
| VA | 903 | 274 | 13 | 3 | 1.4% | 1.1% | 1.4% |
| VT | 323 | 89 | 32 | 2 | 9.9% | 2.2% | 8.3% |
| WA | 1,763 | 335 | 77 | 32 | 4.4% | 9.6% | 5.2% |
| WI | 634 | 313 | 24 | 13 | 3.8% | 4.2% | 3.9% |
| WV | 232 | 245 | 72 | 87 | 31.0% | 35.5% | 33.3% |
| WY | 203 | 47 | 34 | 5 | 16.7% | 10.6% | 15.6% |
| Total | 29,824 | 13,933 | 3,833 | 2,328 | 12.9% | 16.7% | 14.0% |
| a. Size category names follow those used by EPA in the SDWIS/FED database: very small systems are those serving 25-500 persons; and small systems serve 501-3,300. Sources: U.S. EPA, 2002a, 2002b. |

| Table A.2. Number and percentage of medium, large, and very large systems without reliable location data — 2002a |
| --- |
| State | Number of systems | Number of systems with no match in location data | % of systems with no match in location data |
|  | Medium | Large | Very large | Medium | Large | Very large | Medium | Large | Very large | Total medium, large, very large |
| AL | 171 | 92 | 5 | 41 | 16 | 0 | 24.0% | 17.4% | 0.0% | 21.3% |
| AR | 96 | 43 | 1 | 20 | 6 | 0 | 20.8% | 14.0% | 0.0% | 18.6% |
| AZ | 52 | 41 | 8 | 1 | 3 | 0 | 1.9% | 7.3% | 0.0% | 4.0% |
| CA | 227 | 316 | 62 | 3 | 2 | 0 | 1.3% | 0.6% | 0.0% | 0.8% |
| CO | 60 | 54 | 8 | 17 | 16 | 1 | 28.3% | 29.6% | 12.5% | 27.9% |
| CT | 19 | 33 | 5 | 0 | 0 | 0 | 0.0% | 0.0% | 0.0% | 0.0% |
| DE | 15 | 7 | 2 | 8 | 3 | 0 | 53.3% | 42.9% | 0.0% | 45.8% |
| FL | 153 | 199 | 32 | 14 | 1 | 4 | 9.2% | 0.5% | 12.5% | 4.9% |
| GA | 112 | 85 | 12 | 11 | 9 | 2 | 9.8% | 10.6% | 16.7% | 10.5% |
| IA | 79 | 36 | 3 | 13 | 6 | 0 | 16.5% | 16.7% | 0.0% | 16.1% |
| ID | 28 | 13 | 1 | 0 | 0 | 0 | 0.0% | 0.0% | 0.0% | 0.0% |
| IL | 218 | 196 | 9 | 0 | 6 | 1 | 0.0% | 3.1% | 11.1% | 1.7% |
| IN | 120 | 68 | 5 | 25 | 9 | 0 | 20.8% | 13.2% | 0.0% | 17.6% |
| KS | 51 | 26 | 4 | 47 | 23 | 4 | 92.2% | 88.5% | 100.0% | 91.4% |
| KY | 141 | 97 | 3 | 68 | 32 | 0 | 48.2% | 33.0% | 0.0% | 41.5% |
| LA | 144 | 57 | 7 | 28 | 18 | 4 | 19.4% | 31.6% | 57.1% | 24.0% |
| MA | 87 | 152 | 8 | 4 | 29 | 0 | 4.6% | 19.1% | 0.0% | 13.4% |
| MD | 31 | 25 | 4 | 0 | 0 | 1 | 0.0% | 0.0% | 25.0% | 1.7% |
| ME | 19 | 12 | 1 | 1 | 1 | 0 | 5.3% | 8.3% | 0.0% | 6.3% |
| MI | 150 | 121 | 9 | 75 | 95 | 4 | 50.0% | 78.5% | 44.4% | 62.1% |
| MN | 70 | 77 | 2 | 2 | 5 | 0 | 2.9% | 6.5% | 0.0% | 4.7% |
| MO | 126 | 51 | 5 | 19 | 8 | 0 | 15.1% | 15.7% | 0.0% | 14.8% |
| MS | 137 | 47 | 1 | 2 | 0 | 0 | 1.5% | 0.0% | 0.0% | 1.1% |
| MT | 26 | 7 | 0 | 1 | 0 | 0 | 3.8% | 0.0% | na | 3.0% |
| NC | 131 | 98 | 8 | 3 | 0 | 0 | 2.3% | 0.0% | 0.0% | 1.3% |
| ND | 12 | 9 | 0 | 3 | 1 | 0 | 25.0% | 11.1% | na | 19.0% |
| NE | 28 | 12 | 2 | 1 | 1 | 0 | 3.6% | 8.3% | 0.0% | 4.8% |
| NH | 16 | 17 | 1 | 1 | 1 | 0 | 6.3% | 5.9% | 0.0% | 5.9% |
| NJ | 91 | 126 | 12 | 13 | 20 | 1 | 14.3% | 15.9% | 8.3% | 14.8% |
| NM | 32 | 26 | 1 | 5 | 3 | 0 | 15.6% | 11.5% | 0.0% | 13.6% |
| Table A.2. Number and percentage of medium, large, and very large systems without reliable location data — 2002 (cont.)a |
| State | Number of systems | Number of systems with no match in location data | % of systems with no match in location data |
|  | Medium | Large | Very large | Medium | Large | Very large | Medium | Large | Very large | Total medium, large, very large |
| NV | 19 | 7 | 4 | 1 | 3 | 3 | 5.3% | 42.9% | 75.0% | 23.3% |
| NY | 177 | 128 | 20 | 37 | 19 | 3 | 20.9% | 14.8% | 15.0% | 18.2% |
| OH | 148 | 144 | 10 | 2 | 5 | 2 | 1.4% | 3.5% | 20.0% | 3.0% |
| OK | 80 | 42 | 4 | 15 | 2 | 0 | 18.8% | 4.8% | 0.0% | 13.5% |
| OR | 47 | 51 | 4 | 7 | 11 | 1 | 14.9% | 21.6% | 25.0% | 18.6% |
| PA | 180 | 128 | 15 | 1 | 0 | 1 | 0.6% | 0.0% | 6.7% | 0.6% |
| RI | 11 | 13 | 2 | 8 | 3 | 0 | 72.7% | 23.1% | 0.0% | 42.3% |
| SC | 83 | 61 | 4 | 26 | 15 | 1 | 31.3% | 24.6% | 25.0% | 28.4% |
| SD | 21 | 10 | 1 | 1 | 0 | 0 | 4.8% | 0.0% | 0.0% | 3.1% |
| TN | 147 | 100 | 5 | 39 | 16 | 0 | 26.5% | 16.0% | 0.0% | 21.8% |
| TX | 518 | 232 | 26 | 126 | 51 | 4 | 24.3% | 22.0% | 15.4% | 23.3% |
| UT | 48 | 41 | 7 | 3 | 3 | 1 | 6.3% | 7.3% | 14.3% | 7.3% |
| VA | 71 | 57 | 15 | 3 | 3 | 0 | 4.2% | 5.3% | 0.0% | 4.2% |
| VT | 23 | 7 | 0 | 0 | 0 | 0 | 0.0% | 0.0% | na | 0.0% |
| WA | 91 | 85 | 7 | 9 | 21 | 2 | 9.9% | 24.7% | 28.6% | 17.5% |
| WI | 95 | 64 | 4 | 5 | 15 | 2 | 5.3% | 23.4% | 50.0% | 13.5% |
| WV | 58 | 20 | 1 | 11 | 0 | 0 | 19.0% | 0.0% | 0.0% | 13.9% |
| WY | 13 | 9 | 0 | 4 | 3 | 0 | 30.8% | 33.3% | na | 31.8% |
| Total | 4,472 | 3,342 | 350 | 724 | 484 | 42 | 16.2% | 14.5% | 12.0% | 15.3% |
| a. Size category names follow those used by EPA in the SDWIS/FED database: medium systems serve 3,301-10,000; large systems serve 10,001-100,000; and very large systems serve over 100,000. Sources: U.S. EPA, 2002a, 2002b. |

A.4	Calculation of Distance between Systems

To test the feasibility of physically consolidating small systems with nearby larger systems, we calculated the distance from each small system to the nearest facility in a large system. Distance was calculated to a central facility within the nearest system. Since there is no pre-defined central point, we prioritized the types of facilities in large systems and calculated distance by priority. We first checked for the presence of a nearby medium, large, or very large treatment plant (category 1). If multiple treatment plants were present within 25 miles, the distance was set equal to the minimum distance within the category. If no treatment plants were present within 25 miles, then we checked for facilities in category 2, and so on. The categories were prioritized as follows:

- nearest treatment plant within 25 miles

- nearest reservoir within 25 miles

- nearest storage facility within 25 miles

- nearest intake within 25 miles

- nearest well within 25 miles

- nearest pump facility within 25 miles

- nearest treatment plant, reservoir, storage facility, intake, well, or pump facility between 25 to 50 miles.

In cases where no facility in a medium, large, or very large system was found within 50 miles of a small system, that small system was eliminated from the analysis.

A.5	Descriptive Statistics

Once the distance was calculated for each small system, descriptive statistics from several sources were then calculated and summarized. Separate summaries were prepared for rural systems, urban systems, and all systems. Summary statistics were also calculated by system size — very small and small. Combining the three rural/urban categories and two size categories provides a total of six categories for each statistic. Results for these six categories are presented at the national level in Section 4 and for each state in Appendix B.

#### A.5.1	Relevant area

We used GIS software to identify all the census tracts located, fully or partially, within 10 miles of each small water system. This collection of census tracts was defined as the relevant area for each facility in calculating demographic statistics. This area will be larger than the actual service area for some systems and smaller than the actual service area for others, but should accurately capture the differences between populations served by rural and non-rural systems.

### A.5.2	Statistics and data

Descriptive statistics were derived from two sources. Data on population served and number of service connections were obtained from SDWIS/FED and thus represent the actual population served and the actual number of connections, as recorded by the U.S. EPA (2002a). Data on total population, rural population, number of households, income, and poverty levels were obtained at the census tract level from the 2000 U.S. Census of Population (U.S. Census Bureau, 2003).

The demographic data were aggregated across census tracts to calculate for each area: the total percentage of the population designated as rural, the total percentage of households with incomes defined as below the poverty level, and the average of the median household income, weighted by number of households.

### A.5.3	Definition of rural versus nonrural

For this study, we defined a system to be rural if more than 50% of the population in the system area was classified as rural; otherwise we considered the system to be urban.

## A.6	Software Used

Initial database processing was conducted using Microsoft Access 2000. All GIS analysis was conducted using ArcGIS ArcInfo as well as the ArcInfo workstation GRID module (version 8.2). Summary statistics were generated using the SAS System for Windows (version 8).

# Appendix B. State Level Results

| Table B.1. Alabama — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 3 | 0.90 | 2.33 | 4.93 | 2.72 | 208 | 33 | 42,258 | 13.36% |
| Rural areas | 12 | 2.81 | 4.33 | 7.87 | 5.62 | 315 | 99 | 28,722 | 20.13% |
| All | 15 | 2.33 | 3.58 | 7.36 | 5.04 | 294 | 86 | 31,429 | 18.78% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 10 | 1.19 | 3.15 | 5.40 | 3.22 | 2,007 | 667 | 36,420 | 15.70% |
| Rural areas | 69 | 3.87 | 5.96 | 10.08 | 6.84 | 1,860 | 628 | 30,572 | 19.97% |
| All | 79 | 3.51 | 5.60 | 9.86 | 6.38 | 1,879 | 633 | 31,312 | 19.43% |
| a. Percentage of systems with reliable location data and included in sample: 59.8 % of very small systems, 59.8% of small systems, 78.7% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.2. Arizona — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 198 | 1.44 | 4.88 | 10.94 | 7.09 | 159 | 74 | 38,692 | 12.12% |
| Rural areas | 165 | 3.80 | 11.39 | 21.39 | 13.23 | 167 | 66 | 34,004 | 15.08% |
| All | 363 | 2.20 | 7.14 | 16.12 | 9.88 | 163 | 70 | 36,561 | 13.46% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 56 | 1.20 | 3.73 | 9.55 | 6.68 | 1,446 | 544 | 38,856 | 12.07% |
| Rural areas | 39 | 4.27 | 12.87 | 22.93 | 14.36 | 1,098 | 415 | 32,126 | 16.27% |
| All | 95 | 1.75 | 7.49 | 15.70 | 9.84 | 1,303 | 491 | 36,093 | 13.79% |
| a. Percentage of systems with reliable location data and included in sample: 88 % of very small systems, 88% of small systems, 96% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.3. Arkansas — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 8 | 4.30 | 5.60 | 8.37 | 6.97 | 195 | 114 | 36,367 | 14.73% |
| Rural areas | 64 | 6.28 | 10.06 | 14.46 | 10.97 | 250 | 110 | 29,494 | 17.43% |
| All | 72 | 5.56 | 9.64 | 14.27 | 10.53 | 244 | 110 | 30,258 | 17.13% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 12 | 1.70 | 6.15 | 8.27 | 5.42 | 1,471 | 583 | 33,140 | 16.67% |
| Rural areas | 159 | 0.24 | 8.43 | 12.86 | 8.60 | 1,394 | 578 | 29,719 | 17.79% |
| All | 171 | 0.63 | 7.91 | 12.38 | 8.38 | 1,399 | 579 | 29,959 | 17.71% |
| a. Percentage of systems with reliable location data and included in sample: 70.4 % of very small systems, 70.4% of small systems, 81.4% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.4. California — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 1,101 | 1.73 | 4.29 | 9.08 | 6.06 | 144 | 55 | 47,060 | 12.66% |
| Rural areas | 455 | 6.48 | 11.68 | 18.87 | 13.11 | 147 | 66 | 39,313 | 12.66% |
| All | 1,556 | 2.39 | 5.80 | 12.16 | 8.12 | 145 | 58 | 44,794 | 12.66% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 233 | 1.42 | 3.67 | 7.18 | 5.41 | 1,444 | 457 | 45,723 | 12.94% |
| Rural areas | 95 | 6.41 | 10.02 | 16.94 | 12.20 | 1,566 | 503 | 41,977 | 11.20% |
| All | 328 | 2.02 | 5.41 | 9.98 | 7.37 | 1,479 | 471 | 44,638 | 12.43% |
| a. Percentage of systems with reliable location data and included in sample: 94.9 % of very small systems, 94.9% of small systems, 99.2% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.5. Colorado — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 147 | 2.83 | 5.19 | 7.50 | 6.22 | 175 | 69 | 51,996 | 8.09% |
| Rural areas | 158 | 5.72 | 13.35 | 23.55 | 16.06 | 182 | 77 | 42,904 | 10.45% |
| All | 305 | 3.68 | 7.27 | 17.74 | 11.32 | 179 | 73 | 47,286 | 9.32% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 44 | 2.47 | 5.74 | 9.07 | 6.26 | 1,555 | 541 | 53,268 | 7.17% |
| Rural areas | 70 | 11.06 | 15.44 | 23.64 | 18.22 | 1,299 | 455 | 39,000 | 12.42% |
| All | 114 | 5.60 | 11.40 | 20.00 | 13.60 | 1,397 | 488 | 44,507 | 10.39% |
| a. Percentage of systems with reliable location data and included in sample: 76 % of very small systems, 76% of small systems, 72.1% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.6. Connecticut — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 299 | 2.37 | 4.41 | 5.73 | 4.26 | 146 | 42 | 61,488 | 5.96% |
| Rural areas | 75 | 2.81 | 3.76 | 5.61 | 4.95 | 132 | 36 | 54,772 | 6.44% |
| All | 374 | 2.47 | 4.29 | 5.73 | 4.39 | 143 | 41 | 60,142 | 6.06% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 41 | 2.63 | 3.86 | 5.65 | 4.15 | 1,549 | 405 | 62,273 | 5.74% |
| Rural areas | 7 | 8.40 | 11.14 | 15.00 | 11.62 | 1,118 | 426 | 54,283 | 5.65% |
| All | 48 | 2.70 | 4.29 | 6.48 | 5.24 | 1,486 | 408 | 61,108 | 5.73% |
| a. Percentage of systems with reliable location data and included in sample: 100 % of very small systems, 100% of small systems, 100% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.7. Delaware — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 56 | 4.98 | 8.75 | 18.16 | 11.24 | 156 | 58 | 43,592 | 9.08% |
| Rural areas | 29 | 7.42 | 11.62 | 16.47 | 11.25 | 173 | 53 | 39,978 | 10.03% |
| All | 85 | 5.05 | 10.27 | 17.06 | 11.25 | 162 | 57 | 42,359 | 9.40% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 13 | 7.63 | 12.61 | 21.46 | 12.95 | 1,083 | 318 | 43,004 | 8.57% |
| Rural areas | 10 | 9.10 | 15.28 | 16.48 | 13.10 | 1,062 | 277 | 39,925 | 10.06% |
| All | 23 | 7.63 | 14.06 | 19.65 | 13.02 | 1,074 | 300 | 41,665 | 9.22% |
| a. Percentage of systems with reliable location data and included in sample: 49 % of very small systems, 49% of small systems, 54.2% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.8. Florida — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 600 | 1.35 | 2.38 | 3.96 | 2.94 | 185 | 89 | 38,898 | 10.96% |
| Rural areas | 185 | 3.38 | 7.79 | 14.39 | 9.81 | 165 | 76 | 32,291 | 15.12% |
| All | 785 | 1.59 | 2.81 | 5.14 | 4.56 | 181 | 86 | 37,341 | 11.94% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 216 | 1.34 | 2.39 | 4.13 | 3.20 | 1,292 | 462 | 40,520 | 10.74% |
| Rural areas | 113 | 4.32 | 9.49 | 15.18 | 11.23 | 1,538 | 511 | 32,082 | 15.60% |
| All | 329 | 1.70 | 3.48 | 7.62 | 5.96 | 1,377 | 479 | 37,622 | 12.41% |
| a. Percentage of systems with reliable location data and included in sample: 97.8 % of very small systems, 97.8% of small systems, 95.1% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.9. Georgia — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 251 | 1.72 | 3.66 | 5.40 | 3.99 | 136 | 55 | 39,511 | 15.59% |
| Rural areas | 327 | 2.86 | 5.44 | 9.63 | 6.57 | 156 | 67 | 33,795 | 18.11% |
| All | 578 | 2.31 | 4.25 | 7.56 | 5.45 | 147 | 62 | 36,277 | 17.02% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 38 | 1.76 | 3.28 | 6.25 | 4.41 | 1,311 | 417 | 43,131 | 13.08% |
| Rural areas | 127 | 4.54 | 8.73 | 12.32 | 8.95 | 1,347 | 503 | 32,968 | 18.16% |
| All | 165 | 3.22 | 7.72 | 11.30 | 7.90 | 1,339 | 483 | 35,309 | 16.99% |
| a. Percentage of systems with reliable location data and included in sample: 90.4 % of very small systems, 90.4% of small systems, 89.5% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.10. Idaho — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 266 | 1.88 | 3.95 | 8.28 | 5.90 | 121 | 43 | 40,905 | 10.61% |
| Rural areas | 217 | 10.97 | 18.57 | 25.83 | 19.28 | 129 | 59 | 35,339 | 12.40% |
| All | 483 | 3.12 | 8.28 | 18.49 | 11.91 | 125 | 50 | 38,405 | 11.41% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 32 | 2.63 | 3.89 | 8.48 | 5.56 | 1,296 | 518 | 39,947 | 11.40% |
| Rural areas | 47 | 12.21 | 17.49 | 30.65 | 21.88 | 1,305 | 540 | 34,374 | 12.58% |
| All | 79 | 3.77 | 12.17 | 21.25 | 15.27 | 1,301 | 531 | 36,631 | 12.10% |
| a. Percentage of systems with reliable location data and included in sample: 97 % of very small systems, 97% of small systems, 100% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.11. Illinois — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 261 | 0.97 | 2.04 | 4.43 | 3.16 | 198 | 76 | 50,121 | 8.44% |
| Rural areas | 249 | 4.36 | 8.69 | 12.60 | 8.77 | 268 | 121 | 39,712 | 9.06% |
| All | 510 | 1.66 | 4.30 | 9.46 | 5.90 | 232 | 98 | 45,039 | 8.74% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 228 | 1.25 | 3.44 | 6.89 | 4.25 | 1,346 | 491 | 48,166 | 9.45% |
| Rural areas | 310 | 5.38 | 8.90 | 12.66 | 9.22 | 1,198 | 515 | 39,256 | 9.45% |
| All | 538 | 2.60 | 6.54 | 10.64 | 7.11 | 1,260 | 505 | 43,032 | 9.45% |
| a. Percentage of systems with reliable location data and included in sample: 98.7 % of very small systems, 98.7% of small systems, 98.3% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.12. Indiana — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 144 | 3.54 | 5.44 | 8.64 | 6.36 | 141 | 49 | 46,553 | 8.75% |
| Rural areas | 155 | 3.78 | 6.39 | 10.05 | 7.15 | 164 | 59 | 42,565 | 7.21% |
| All | 299 | 3.55 | 6.01 | 9.31 | 6.77 | 153 | 54 | 44,486 | 7.95% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 75 | 4.01 | 7.19 | 9.31 | 7.32 | 1,585 | 544 | 44,419 | 9.11% |
| Rural areas | 159 | 5.51 | 9.03 | 11.85 | 9.76 | 1,299 | 467 | 41,724 | 7.91% |
| All | 234 | 5.14 | 8.22 | 11.43 | 8.98 | 1,391 | 492 | 42,588 | 8.29% |
| a. Percentage of systems with reliable location data and included in sample: 76.3 % of very small systems, 76.3% of small systems, 82.4% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.13. Iowa — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 164 | 3.52 | 8.09 | 15.19 | 9.34 | 133 | 49 | 42,557 | 9.59% |
| Rural areas | 275 | 7.59 | 12.16 | 16.82 | 12.27 | 200 | 93 | 39,273 | 8.38% |
| All | 439 | 6.14 | 10.78 | 16.25 | 11.18 | 175 | 77 | 40,500 | 8.84% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 37 | 6.40 | 9.50 | 13.85 | 10.58 | 1,099 | 380 | 43,799 | 9.49% |
| Rural areas | 169 | 10.91 | 14.73 | 19.25 | 14.64 | 1,272 | 537 | 39,449 | 8.13% |
| All | 206 | 9.89 | 13.98 | 18.93 | 13.91 | 1,241 | 509 | 40,231 | 8.37% |
| a. Percentage of systems with reliable location data and included in sample: 82.4 % of very small systems, 82.4% of small systems, 83.9% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.14. Kansas — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 12 | 11.66 | 28.00 | 43.06 | 26.56 | 162 | 54 | 38,154 | 11.45% |
| Rural areas | 12 | 22.92 | 32.33 | 37.23 | 31.22 | 234 | 106 | 36,758 | 9.05% |
| All | 24 | 20.68 | 30.48 | 40.13 | 28.89 | 198 | 80 | 37,456 | 10.25% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 2 | 20.33 | 24.85 | 29.38 | 24.85 | 1,439 | 215 | 39,359 | 11.41% |
| Rural areas | 10 | 21.42 | 31.98 | 33.40 | 28.78 | 1,315 | 432 | 40,384 | 8.46% |
| All | 12 | 20.87 | 30.34 | 33.34 | 28.12 | 1,336 | 396 | 40,213 | 8.96% |
| a. Percentage of systems with reliable location data and included in sample: 8.1 % of very small systems, 8.1% of small systems, 8.6% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.15. Kentucky — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 4 | 2.53 | 8.66 | 13.54 | 8.04 | 172 | 8 | 49,546 | 8.58% |
| Rural areas | 28 | 6.08 | 8.16 | 12.66 | 9.34 | 239 | 61 | 27,247 | 22.07% |
| All | 32 | 5.61 | 8.16 | 13.13 | 9.17 | 230 | 55 | 30,034 | 20.39% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 2 | 3.25 | 4.68 | 6.12 | 4.68 | 1,747 | 558 | 35,711 | 13.06% |
| Rural areas | 49 | 4.55 | 7.48 | 10.95 | 7.92 | 1,806 | 564 | 29,485 | 19.38% |
| All | 51 | 3.95 | 7.31 | 10.95 | 7.79 | 1,804 | 564 | 29,729 | 19.13% |
| a. Percentage of systems with reliable location data and included in sample: 45.1 % of very small systems, 45.1% of small systems, 58.5% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.16. Louisiana — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 230 | 3.17 | 8.61 | 17.24 | 10.05 | 163 | 48 | 40,442 | 14.72% |
| Rural areas | 116 | 5.16 | 10.91 | 16.52 | 11.18 | 257 | 72 | 31,189 | 19.67% |
| All | 346 | 3.39 | 9.50 | 17.05 | 10.43 | 194 | 56 | 37,340 | 16.38% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 67 | 3.47 | 8.03 | 14.99 | 10.11 | 1,499 | 415 | 37,132 | 17.81% |
| Rural areas | 181 | 7.07 | 13.96 | 19.02 | 13.06 | 1,527 | 432 | 29,837 | 20.93% |
| All | 248 | 5.77 | 12.32 | 18.27 | 12.26 | 1,519 | 428 | 31,808 | 20.09% |
| a. Percentage of systems with reliable location data and included in sample: 84.6 % of very small systems, 84.6% of small systems, 76% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.17. Maine — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 22 | 6.80 | 11.64 | 16.66 | 11.39 | 109 | 44 | 40,829 | 11.30% |
| Rural areas | 167 | 8.13 | 13.19 | 20.25 | 15.22 | 113 | 44 | 35,684 | 12.42% |
| All | 189 | 8.08 | 12.49 | 19.19 | 14.77 | 113 | 44 | 36,283 | 12.29% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 4 | 3.73 | 7.90 | 8.72 | 6.23 | 1,275 | 510 | 42,838 | 9.48% |
| Rural areas | 59 | 10.59 | 16.10 | 22.59 | 17.73 | 1,509 | 602 | 34,514 | 12.46% |
| All | 63 | 8.94 | 15.59 | 21.98 | 17.00 | 1,494 | 596 | 35,042 | 12.27% |
| a. Percentage of systems with reliable location data and included in sample: 91.2 % of very small systems, 91.2% of small systems, 93.8% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.18. Maryland — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 146 | 2.07 | 3.50 | 6.07 | 4.46 | 169 | 59 | 55,602 | 7.00% |
| Rural areas | 106 | 4.78 | 7.22 | 11.59 | 8.24 | 163 | 60 | 49,601 | 8.53% |
| All | 252 | 2.53 | 4.96 | 8.81 | 6.05 | 166 | 59 | 53,078 | 7.65% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 39 | 1.65 | 4.00 | 5.40 | 4.01 | 1,285 | 422 | 60,289 | 5.69% |
| Rural areas | 39 | 5.33 | 7.79 | 13.45 | 8.88 | 1,274 | 452 | 50,229 | 8.01% |
| All | 78 | 3.09 | 5.36 | 9.37 | 6.45 | 1,279 | 437 | 55,259 | 6.85% |
| a. Percentage of systems with reliable location data and included in sample: 90.8 % of very small systems, 90.8% of small systems, 98.3% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.19. Massachusetts — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 126 | 1.48 | 2.84 | 4.40 | 3.25 | 115 | 37 | 54,845 | 7.99% |
| Rural areas | 26 | 4.67 | 7.28 | 10.43 | 7.16 | 138 | 38 | 46,429 | 7.94% |
| All | 152 | 1.65 | 3.29 | 5.61 | 3.91 | 119 | 37 | 53,405 | 7.98% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 33 | 2.05 | 2.50 | 5.17 | 3.43 | 1,773 | 560 | 52,200 | 8.27% |
| Rural areas | 16 | 3.52 | 4.94 | 9.40 | 6.26 | 1,264 | 432 | 47,097 | 7.64% |
| All | 49 | 2.09 | 3.91 | 6.04 | 4.35 | 1,607 | 518 | 50,534 | 8.06% |
| a. Percentage of systems with reliable location data and included in sample: 92.1 % of very small systems, 92.1% of small systems, 86.6% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.20. Michigan — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 92 | 4.69 | 14.37 | 19.76 | 12.65 | 169 | 55 | 56,934 | 6.99% |
| Rural areas | 138 | 6.60 | 16.51 | 24.67 | 18.09 | 174 | 68 | 40,066 | 9.21% |
| All | 230 | 5.98 | 14.90 | 22.55 | 15.91 | 172 | 63 | 46,813 | 8.32% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 42 | 4.13 | 11.50 | 15.79 | 11.06 | 1,264 | 465 | 53,382 | 8.34% |
| Rural areas | 94 | 11.42 | 17.41 | 22.95 | 17.81 | 1,429 | 570 | 40,680 | 8.94% |
| All | 136 | 9.72 | 15.37 | 22.03 | 15.72 | 1,378 | 538 | 44,603 | 8.76% |
| a. Percentage of systems with reliable location data and included in sample: 64 % of very small systems, 64% of small systems, 37.9% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.21. Minnesota — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 98 | 2.25 | 7.99 | 15.14 | 9.64 | 172 | 48 | 52,731 | 6.91% |
| Rural areas | 224 | 8.91 | 14.88 | 20.95 | 15.50 | 190 | 77 | 40,130 | 9.25% |
| All | 322 | 6.63 | 12.97 | 19.65 | 13.71 | 185 | 68 | 43,965 | 8.54% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 50 | 4.46 | 9.08 | 17.29 | 10.74 | 1,337 | 397 | 56,363 | 6.21% |
| Rural areas | 132 | 10.30 | 16.40 | 21.67 | 16.52 | 1,333 | 518 | 41,127 | 8.79% |
| All | 182 | 8.78 | 15.07 | 21.03 | 14.93 | 1,334 | 485 | 45,313 | 8.08% |
| a. Percentage of systems with reliable location data and included in sample: 95.7 % of very small systems, 95.7% of small systems, 95.3% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.22. Mississippi — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 51 | 1.59 | 2.94 | 5.10 | 3.55 | 207 | 72 | 33,219 | 20.37% |
| Rural areas | 149 | 3.37 | 8.43 | 13.46 | 8.73 | 274 | 99 | 27,282 | 24.46% |
| All | 200 | 2.43 | 5.90 | 11.94 | 7.41 | 257 | 92 | 28,796 | 23.42% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 64 | 1.81 | 3.37 | 5.01 | 3.57 | 1,453 | 441 | 34,449 | 19.35% |
| Rural areas | 322 | 4.36 | 7.11 | 10.96 | 8.06 | 1,407 | 492 | 29,045 | 21.39% |
| All | 386 | 3.72 | 6.07 | 10.09 | 7.31 | 1,415 | 483 | 29,941 | 21.05% |
| a. Percentage of systems with reliable location data and included in sample: 97.1 % of very small systems, 97.1% of small systems, 98.9% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.23. Missouri — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 137 | 3.28 | 5.41 | 8.33 | 6.19 | 135 | 54 | 44,507 | 9.51% |
| Rural areas | 555 | 6.22 | 10.80 | 16.07 | 11.65 | 157 | 68 | 33,975 | 12.72% |
| All | 692 | 5.34 | 9.55 | 14.74 | 10.57 | 153 | 66 | 36,060 | 12.08% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 40 | 4.90 | 6.85 | 9.47 | 7.47 | 1,608 | 527 | 40,863 | 11.08% |
| Rural areas | 243 | 7.96 | 12.67 | 17.95 | 13.25 | 1,333 | 568 | 33,281 | 13.65% |
| All | 283 | 7.14 | 12.02 | 17.19 | 12.43 | 1,372 | 562 | 34,352 | 13.29% |
| a. Percentage of systems with reliable location data and included in sample: 80.9 % of very small systems, 80.9% of small systems, 85.2% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.24. Montana — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 135 | 2.25 | 7.79 | 14.11 | 8.59 | 132 | 44 | 36,139 | 13.04% |
| Rural areas | 205 | 10.38 | 16.99 | 32.76 | 21.57 | 133 | 47 | 32,450 | 14.16% |
| All | 340 | 5.52 | 14.38 | 23.77 | 16.42 | 133 | 46 | 33,915 | 13.72% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 16 | 3.39 | 6.24 | 10.13 | 7.21 | 1,226 | 341 | 35,729 | 13.21% |
| Rural areas | 40 | 20.78 | 31.29 | 37.80 | 29.11 | 1,279 | 502 | 31,454 | 14.37% |
| All | 56 | 10.21 | 23.00 | 33.78 | 22.85 | 1,264 | 456 | 32,675 | 14.03% |
| a. Percentage of systems with reliable location data and included in sample: 96 % of very small systems, 96% of small systems, 97% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.25. Nebraska — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 79 | 0.56 | 1.43 | 7.43 | 5.01 | 186 | 68 | 44,255 | 8.81% |
| Rural areas | 180 | 10.76 | 16.25 | 21.81 | 16.88 | 224 | 116 | 35,307 | 10.53% |
| All | 259 | 4.60 | 11.96 | 19.58 | 13.26 | 213 | 101 | 38,036 | 10.00% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 26 | 1.72 | 5.51 | 11.09 | 6.94 | 1,291 | 510 | 43,083 | 8.54% |
| Rural areas | 108 | 9.51 | 16.23 | 22.86 | 16.75 | 1,120 | 500 | 35,427 | 10.53% |
| All | 134 | 7.29 | 13.56 | 20.58 | 14.85 | 1,153 | 502 | 36,913 | 10.15% |
| a. Percentage of systems with reliable location data and included in sample: 94.1 % of very small systems, 94.1% of small systems, 95.2% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.26. Nevada — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 74 | 1.77 | 7.11 | 14.15 | 8.93 | 135 | 53 | 46,716 | 9.17% |
| Rural areas | 27 | 3.14 | 10.58 | 30.34 | 16.86 | 125 | 56 | 42,893 | 10.65% |
| All | 101 | 1.86 | 8.75 | 14.82 | 11.05 | 132 | 54 | 45,694 | 9.57% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 14 | 5.23 | 13.71 | 17.94 | 12.80 | 1,904 | 673 | 47,433 | 9.00% |
| Rural areas | 9 | 20.69 | 22.87 | 33.03 | 26.80 | 1,510 | 427 | 42,449 | 11.83% |
| All | 23 | 10.20 | 17.11 | 22.87 | 18.28 | 1,750 | 577 | 45,483 | 10.11% |
| a. Percentage of systems with reliable location data and included in sample: 73.2 % of very small systems, 73.2% of small systems, 76.7% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.27. New Hampshire — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 188 | 2.25 | 3.36 | 5.21 | 3.98 | 120 | 47 | 56,764 | 6.41% |
| Rural areas | 329 | 4.29 | 6.11 | 9.20 | 7.33 | 120 | 45 | 43,282 | 7.76% |
| All | 517 | 3.16 | 5.04 | 8.00 | 6.11 | 120 | 46 | 48,184 | 7.27% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 16 | 2.82 | 4.72 | 6.46 | 4.69 | 1,694 | 671 | 55,699 | 6.35% |
| Rural areas | 57 | 5.69 | 8.47 | 12.09 | 9.67 | 1,308 | 462 | 44,264 | 7.55% |
| All | 73 | 4.83 | 7.16 | 11.26 | 8.58 | 1,392 | 508 | 46,770 | 7.29% |
| a. Percentage of systems with reliable location data and included in sample: 90.4 % of very small systems, 90.4% of small systems, 94.1% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.28. New Jersey — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 153 | 1.19 | 2.10 | 4.17 | 2.77 | 157 | 66 | 60,203 | 6.05% |
| Rural areas | 13 | 4.13 | 6.49 | 8.38 | 6.36 | 136 | 46 | 64,732 | 5.04% |
| All | 166 | 1.20 | 2.27 | 4.32 | 3.05 | 156 | 64 | 60,558 | 5.97% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 79 | 1.09 | 2.24 | 4.14 | 2.78 | 1,529 | 608 | 61,769 | 5.77% |
| Rural areas | 7 | 2.94 | 6.70 | 7.36 | 5.73 | 1,453 | 471 | 64,186 | 4.98% |
| All | 86 | 1.25 | 2.49 | 4.26 | 3.02 | 1,523 | 597 | 61,966 | 5.70% |
| a. Percentage of systems with reliable location data and included in sample: 87.1 % of very small systems, 87.1% of small systems, 85.2% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.29. New Mexico — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 93 | 2.94 | 6.09 | 9.37 | 7.38 | 140 | 52 | 39,138 | 15.38% |
| Rural areas | 118 | 6.64 | 15.65 | 23.01 | 16.95 | 174 | 62 | 31,803 | 19.58% |
| All | 211 | 4.08 | 8.89 | 18.71 | 12.73 | 159 | 58 | 35,036 | 17.73% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 29 | 2.06 | 4.04 | 7.41 | 5.26 | 1,216 | 348 | 35,132 | 17.11% |
| Rural areas | 31 | 6.77 | 11.73 | 21.62 | 14.26 | 1,181 | 421 | 33,218 | 17.26% |
| All | 60 | 3.02 | 7.03 | 12.97 | 9.91 | 1,198 | 386 | 34,143 | 17.19% |
| a. Percentage of systems with reliable location data and included in sample: 66.4 % of very small systems, 66.4% of small systems, 86.4% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.30. New York — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 526 | 2.56 | 4.75 | 7.40 | 5.72 | 162 | 53 | 54,481 | 8.46% |
| Rural areas | 587 | 5.61 | 9.47 | 14.67 | 10.45 | 138 | 47 | 39,273 | 10.69% |
| All | 1,113 | 3.72 | 6.70 | 11.63 | 8.22 | 149 | 50 | 46,460 | 9.64% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 141 | 2.01 | 3.68 | 6.79 | 5.09 | 1,523 | 447 | 54,216 | 8.37% |
| Rural areas | 225 | 6.74 | 10.14 | 14.41 | 11.06 | 1,275 | 423 | 38,527 | 10.62% |
| All | 366 | 3.72 | 7.66 | 12.35 | 8.76 | 1,370 | 432 | 44,571 | 9.75% |
| a. Percentage of systems with reliable location data and included in sample: 72.8 % of very small systems, 72.8% of small systems, 81.8% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.31. North Carolina — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 884 | 3.12 | 5.91 | 9.47 | 7.17 | 136 | 58 | 45,967 | 9.95% |
| Rural areas | 523 | 4.69 | 9.79 | 18.65 | 11.45 | 135 | 53 | 36,741 | 13.32% |
| All | 1,407 | 3.58 | 6.82 | 13.20 | 8.76 | 136 | 56 | 42,537 | 11.20% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 160 | 0.10 | 7.96 | 17.63 | 8.36 | 897 | 367 | 50,022 | 9.22% |
| Rural areas | 189 | 0.70 | 11.66 | 17.18 | 10.39 | 1,462 | 630 | 35,043 | 14.80% |
| All | 349 | 0.21 | 10.59 | 17.45 | 9.46 | 1,203 | 509 | 41,910 | 12.24% |
| a. Percentage of systems with reliable location data and included in sample: 97.9 % of very small systems, 97.9% of small systems, 98.7% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.32. North Dakota — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 17 | 3.94 | 4.59 | 8.23 | 5.53 | 108 | 36 | 39,376 | 11.48% |
| Rural areas | 72 | 18.94 | 26.26 | 34.40 | 26.56 | 188 | 98 | 33,201 | 13.25% |
| All | 89 | 10.35 | 21.74 | 33.08 | 22.55 | 173 | 87 | 34,381 | 12.91% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 5 | 6.09 | 6.45 | 6.70 | 6.09 | 991 | 276 | 39,228 | 10.79% |
| Rural areas | 54 | 21.00 | 27.63 | 35.00 | 27.06 | 1,354 | 557 | 34,195 | 11.55% |
| All | 59 | 14.32 | 24.97 | 34.95 | 25.28 | 1,323 | 534 | 34,622 | 11.49% |
| a. Percentage of systems with reliable location data and included in sample: 80.7 % of very small systems, 80.7% of small systems, 81% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.33. Ohio — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 191 | 2.69 | 4.40 | 6.43 | 4.55 | 181 | 71 | 44,510 | 9.22% |
| Rural areas | 153 | 2.93 | 4.97 | 8.13 | 5.79 | 189 | 69 | 38,833 | 10.88% |
| All | 344 | 2.74 | 4.58 | 7.13 | 5.10 | 184 | 70 | 41,985 | 9.96% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 91 | 2.15 | 3.86 | 6.37 | 4.51 | 1,407 | 500 | 45,417 | 9.02% |
| Rural areas | 171 | 4.84 | 7.48 | 10.08 | 7.46 | 1,433 | 567 | 38,441 | 11.13% |
| All | 262 | 3.51 | 6.36 | 9.10 | 6.44 | 1,424 | 544 | 40,864 | 10.40% |
| a. Percentage of systems with reliable location data and included in sample: 98.1 % of very small systems, 98.1% of small systems, 97% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.34. Oklahoma — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 68 | 1.85 | 3.32 | 6.47 | 4.58 | 169 | 67 | 36,320 | 14.21% |
| Rural areas | 205 | 6.12 | 10.43 | 16.11 | 11.51 | 212 | 102 | 31,638 | 15.31% |
| All | 273 | 4.23 | 8.23 | 13.42 | 9.78 | 202 | 94 | 32,804 | 15.03% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 34 | 4.84 | 7.26 | 9.41 | 7.54 | 1,575 | 551 | 34,390 | 15.40% |
| Rural areas | 205 | 8.38 | 11.75 | 16.85 | 13.03 | 1,422 | 613 | 30,467 | 16.10% |
| All | 239 | 7.38 | 10.89 | 16.18 | 12.25 | 1,443 | 604 | 31,025 | 16.00% |
| a. Percentage of systems with reliable location data and included in sample: 64.6 % of very small systems, 64.6% of small systems, 86.5% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.35. Oregon — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 271 | 4.92 | 9.25 | 15.01 | 10.42 | 126 | 54 | 42,342 | 10.51% |
| Rural areas | 158 | 8.91 | 16.35 | 22.96 | 17.32 | 150 | 72 | 38,545 | 11.15% |
| All | 429 | 6.37 | 10.58 | 18.72 | 12.96 | 135 | 60 | 40,943 | 10.74% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 40 | 6.92 | 10.37 | 15.94 | 11.62 | 1,431 | 521 | 40,643 | 10.49% |
| Rural areas | 56 | 9.54 | 14.07 | 19.40 | 15.65 | 1,428 | 567 | 39,275 | 10.74% |
| All | 96 | 7.62 | 12.69 | 17.86 | 13.97 | 1,429 | 548 | 39,845 | 10.63% |
| a. Percentage of systems with reliable location data and included in sample: 88.1 % of very small systems, 88.1% of small systems, 81.4% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.36. Pennsylvania — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 481 | 1.59 | 3.31 | 5.15 | 3.70 | 159 | 59 | 46,412 | 8.16% |
| Rural areas | 539 | 3.52 | 6.31 | 9.49 | 6.86 | 171 | 61 | 38,390 | 10.03% |
| All | 1,020 | 2.36 | 4.60 | 7.45 | 5.37 | 165 | 60 | 42,173 | 9.15% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 182 | 1.02 | 2.25 | 4.68 | 3.10 | 1,539 | 493 | 46,701 | 8.60% |
| Rural areas | 204 | 2.84 | 5.82 | 9.86 | 6.61 | 1,341 | 490 | 36,911 | 10.37% |
| All | 386 | 1.55 | 4.00 | 7.17 | 4.95 | 1,434 | 492 | 41,527 | 9.53% |
| a. Percentage of systems with reliable location data and included in sample: 98.8 % of very small systems, 98.8% of small systems, 99.4% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.37. Rhode Island — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 33 | 2.01 | 4.15 | 6.40 | 4.26 | 141 | 38 | 58,708 | 6.52% |
| Rural areas | 5 | 6.69 | 7.59 | 7.77 | 7.51 | 94 | 46 | 58,579 | 5.05% |
| All | 38 | 2.37 | 4.24 | 7.59 | 4.69 | 135 | 39 | 58,691 | 6.32% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 8 | 1.95 | 5.23 | 8.05 | 5.61 | 1,610 | 670 | 53,685 | 8.09% |
| Rural areas | 0 | na | na | na | na | na | na | na | na |
| All | 8 | 1.95 | 5.23 | 8.05 | 5.61 | 1,610 | 670 | 53,685 | 8.09% |
| a. Percentage of systems with reliable location data and included in sample: 83.3 % of very small systems, 83.3% of small systems, 57.7% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.38. South Carolina — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 202 | 4.11 | 6.71 | 10.06 | 7.23 | 117 | 50 | 44,287 | 10.99% |
| Rural areas | 91 | 6.00 | 8.06 | 13.20 | 9.41 | 135 | 53 | 35,406 | 16.53% |
| All | 293 | 4.44 | 7.21 | 10.49 | 7.91 | 123 | 51 | 41,529 | 12.71% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 33 | 2.65 | 4.70 | 7.69 | 5.76 | 1,278 | 477 | 40,192 | 13.61% |
| Rural areas | 56 | 6.38 | 12.50 | 17.06 | 12.06 | 1,427 | 546 | 32,547 | 18.75% |
| All | 89 | 4.70 | 8.07 | 14.84 | 9.72 | 1,372 | 521 | 35,382 | 16.85% |
| a. Percentage of systems with reliable location data and included in sample: 72.9 % of very small systems, 72.9% of small systems, 71.6% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.39. South Dakota — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 90 | 2.11 | 3.28 | 6.28 | 4.11 | 140 | 55 | 37,050 | 11.30% |
| Rural areas | 135 | 8.93 | 15.97 | 22.15 | 16.62 | 181 | 80 | 33,520 | 12.63% |
| All | 225 | 3.11 | 8.10 | 17.46 | 11.62 | 165 | 70 | 34,932 | 12.10% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 21 | 3.20 | 5.06 | 7.64 | 5.52 | 1,482 | 601 | 38,394 | 10.73% |
| Rural areas | 60 | 10.54 | 15.78 | 22.88 | 17.56 | 1,232 | 579 | 33,326 | 12.82% |
| All | 81 | 6.35 | 12.97 | 21.26 | 14.44 | 1,297 | 585 | 34,640 | 12.28% |
| a. Percentage of systems with reliable location data and included in sample: 98.4 % of very small systems, 98.4% of small systems, 96.9% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.40. Tennessee — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 39 | 0.55 | 3.75 | 8.00 | 4.60 | 216 | 74 | 40,489 | 10.61% |
| Rural areas | 10 | 5.01 | 7.55 | 14.37 | 8.88 | 188 | 59 | 28,534 | 18.19% |
| All | 49 | 0.90 | 4.36 | 8.83 | 5.48 | 210 | 71 | 34,197 | 14.60% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 75 | 0.81 | 3.65 | 5.94 | 4.16 | 1,606 | 622 | 48,580 | 8.00% |
| Rural areas | 18 | 3.58 | 6.84 | 10.53 | 7.16 | 1,446 | 659 | 30,736 | 18.63% |
| All | 93 | 1.10 | 4.21 | 6.97 | 4.74 | 1,575 | 629 | 38,219 | 14.17% |
| a. Percentage of systems with reliable location data and included in sample: 54.3 % of very small systems, 54.3% of small systems, 78.2% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.41. Texas — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 777 | 3.59 | 8.06 | 13.33 | 9.13 | 158 | 54 | 47,932 | 11.59% |
| Rural areas | 700 | 5.64 | 10.88 | 16.28 | 11.90 | 190 | 69 | 38,992 | 12.98% |
| All | 1,477 | 4.41 | 9.21 | 14.87 | 10.45 | 173 | 61 | 43,695 | 12.25% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 383 | 3.78 | 6.95 | 13.05 | 8.94 | 1,546 | 523 | 48,654 | 12.02% |
| Rural areas | 386 | 6.49 | 12.10 | 17.09 | 12.55 | 1,352 | 498 | 36,380 | 14.15% |
| All | 769 | 4.76 | 9.26 | 15.92 | 10.75 | 1,449 | 511 | 42,493 | 13.09% |
| a. Percentage of systems with reliable location data and included in sample: 76 % of very small systems, 76% of small systems, 76.7% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.42. Utah — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 77 | 4.23 | 8.34 | 10.88 | 9.20 | 188 | 71 | 46,335 | 9.52% |
| Rural areas | 90 | 14.25 | 22.89 | 33.55 | 24.58 | 207 | 93 | 39,828 | 9.96% |
| All | 167 | 7.59 | 13.94 | 23.99 | 17.49 | 198 | 83 | 42,828 | 9.76% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 31 | 6.57 | 9.84 | 15.24 | 11.21 | 1,345 | 379 | 47,625 | 8.85% |
| Rural areas | 40 | 14.20 | 22.48 | 34.51 | 24.57 | 1,495 | 514 | 39,376 | 10.61% |
| All | 71 | 9.40 | 15.24 | 27.22 | 18.74 | 1,429 | 455 | 42,977 | 9.84% |
| a. Percentage of systems with reliable location data and included in sample: 93.1 % of very small systems, 93.1% of small systems, 92.7% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.43. Vermont — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 27 | 0.00 | 3.37 | 8.84 | 4.61 | 177 | 68 | 46,452 | 9.40% |
| Rural areas | 214 | 5.21 | 9.33 | 13.74 | 9.75 | 156 | 49 | 41,228 | 9.18% |
| All | 241 | 4.03 | 8.99 | 13.02 | 9.18 | 158 | 51 | 41,814 | 9.21% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 7 | 0.00 | 9.33 | 11.59 | 6.17 | 1,142 | 255 | 49,873 | 7.92% |
| Rural areas | 52 | 6.81 | 9.60 | 14.98 | 10.78 | 1,340 | 336 | 39,806 | 9.91% |
| All | 59 | 6.38 | 9.33 | 14.40 | 10.24 | 1,317 | 326 | 41,000 | 9.68% |
| a. Percentage of systems with reliable location data and included in sample: 96.6 % of very small systems, 96.6% of small systems, 100% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.44. Virginia — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 255 | 3.51 | 5.65 | 8.71 | 6.26 | 155 | 52 | 44,197 | 10.98% |
| Rural areas | 446 | 4.77 | 11.11 | 15.14 | 11.16 | 135 | 47 | 38,326 | 12.35% |
| All | 701 | 4.07 | 8.37 | 13.55 | 9.38 | 142 | 49 | 40,462 | 11.85% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 65 | 2.96 | 4.12 | 7.31 | 5.30 | 1,128 | 297 | 46,920 | 10.25% |
| Rural areas | 165 | 3.26 | 9.40 | 13.51 | 9.56 | 1,396 | 484 | 36,067 | 14.02% |
| All | 230 | 3.11 | 6.88 | 12.08 | 8.36 | 1,320 | 431 | 39,134 | 12.95% |
| a. Percentage of systems with reliable location data and included in sample: 96.4 % of very small systems, 96.4% of small systems, 95.8% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.45. Washington — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 824 | 1.50 | 3.13 | 5.47 | 3.89 | 119 | 48 | 47,316 | 9.24% |
| Rural areas | 486 | 6.18 | 11.19 | 17.17 | 12.50 | 131 | 62 | 40,285 | 11.76% |
| All | 1,310 | 2.05 | 4.82 | 9.34 | 7.09 | 123 | 53 | 44,708 | 10.17% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 103 | 1.21 | 3.43 | 5.75 | 4.50 | 1,343 | 467 | 46,485 | 9.73% |
| Rural areas | 111 | 8.19 | 14.63 | 20.21 | 15.45 | 1,277 | 494 | 40,100 | 11.82% |
| All | 214 | 3.16 | 7.13 | 15.81 | 10.18 | 1,309 | 481 | 43,173 | 10.81% |
| a. Percentage of systems with reliable location data and included in sample: 90.1 % of very small systems, 90.1% of small systems, 82.5% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.46. West Virginia — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 7 | 1.77 | 3.69 | 5.70 | 4.50 | 164 | 58 | 35,558 | 12.77% |
| Rural areas | 114 | 5.46 | 10.69 | 15.43 | 10.91 | 184 | 72 | 30,342 | 18.45% |
| All | 121 | 5.36 | 10.38 | 15.21 | 10.54 | 183 | 71 | 30,644 | 18.12% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 18 | 2.13 | 3.46 | 6.64 | 4.56 | 1,955 | 719 | 31,112 | 15.95% |
| Rural areas | 111 | 5.72 | 10.88 | 16.23 | 11.07 | 1,464 | 588 | 28,592 | 19.06% |
| All | 129 | 4.04 | 9.03 | 15.54 | 10.16 | 1,532 | 606 | 28,944 | 18.63% |
| a. Percentage of systems with reliable location data and included in sample: 64.5 % of very small systems, 64.5% of small systems, 86.1% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.47. Wisconsin — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 236 | 1.73 | 3.26 | 5.62 | 3.72 | 115 | 49 | 50,219 | 7.43% |
| Rural areas | 219 | 4.99 | 9.43 | 15.27 | 10.66 | 143 | 56 | 41,657 | 7.98% |
| All | 455 | 2.48 | 5.14 | 9.43 | 7.06 | 128 | 53 | 46,098 | 7.69% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 43 | 2.73 | 5.00 | 6.95 | 5.09 | 1,387 | 511 | 50,317 | 6.17% |
| Rural areas | 137 | 7.76 | 12.15 | 16.00 | 12.78 | 1,312 | 497 | 42,551 | 7.79% |
| All | 180 | 5.85 | 9.91 | 14.86 | 10.95 | 1,330 | 500 | 44,406 | 7.41% |
| a. Percentage of systems with reliable location data and included in sample: 95.8 % of very small systems, 95.8% of small systems, 86.5% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

| Table B.48. Wyoming — Summary of key statistics for small and very small water systems in rural and urban areas |
| --- |
| System type | Sample sizea | Distance (in miles) to nearest medium, large or very large facility | Population served | Service connections | Household incomeb | Poverty ratec |
|  |  | 25th percentile | Median | 75th percentile | Mean |  |  |  |  |
| Very small systems (25 to 500 persons served) |
| Metro areas | 45 | 2.18 | 5.34 | 19.88 | 12.12 | 147 | 61 | 44,596 | 8.93% |
| Rural areas | 60 | 4.58 | 20.65 | 30.68 | 19.83 | 170 | 87 | 40,465 | 10.29% |
| All | 105 | 3.26 | 11.29 | 28.55 | 16.53 | 160 | 76 | 42,235 | 9.71% |
| Small systems (501 to 3,300 persons served) |
| Metro areas | 5 | 17.94 | 20.30 | 41.29 | 24.80 | 1,346 | 613 | 38,363 | 12.34% |
| Rural areas | 18 | 12.59 | 23.18 | 32.59 | 22.24 | 1,489 | 603 | 39,835 | 10.18% |
| All | 23 | 12.59 | 22.87 | 33.30 | 22.80 | 1,458 | 605 | 39,515 | 10.65% |
| a. Percentage of systems with reliable location data and included in sample: 89.4 % of very small systems, 89.4% of small systems, 68.2% of large systems (a smaller percentage may be reported in the sample size due to cases where no larger system was found within 50 miles) b. Mean value of median household income in all census tracts within 10 miles of water system, weighted by number of households. c. Mean percent of households in all census tracts within 10 miles of water system. Sources: U.S. EPA, 2002a, 2002b; U.S. Census Bureau, 2003. |

# Footnotes

. In this report, we use the term “small water system” to generically describe both very small (25-500 served) and small (501-3,300 served) systems.

. Due to security concerns, much of the data in SDWIS/FED are available only via special request.

. For this study, we defined a system is defined to be rural if more than 50% of the population in the system area was classified as rural; otherwise we considered the system to be urban.

. Because of security concerns, much of the data in SDWIS/FED are available only via special request.

# Text boxes

Copyright © 2004 by National Rural Water Association. Compilation copyright © 2004 by National Rural Water Association. All rights reserved. No part of this paper may be reproduced or transmitted in any form or by any means, electronic or mechanical, including photocopying, recording, or by any information storage and retrieval system, without permission in writing from the publisher. 

National Rural Water Association, 2915 South 13th Street, Duncan, OK 73533, 580-252-0629, FAX 580-255-4476
http://www.nrwa.org, Printed in the United States of America.